Since the coefficients of the transfer function polynomials are real the zeros and poles consist of either real roots or conjugate pairs. One conjugate pair of zeros can be combined with one pair of poles to form a single bi-quad stage with real coefficients. For more than one bi-quad stage it doesn’t matter which conjugate pair of zeros is associated with a conjugate pair of poles, just as long as there all represented.

The function for a single bi-quad stage.
f sub i(s) = {(s - z sub i)(s - hat z sub i)} over {(s - p sub i)(s- hat p sub i)} = {n sub i (s)}over{d sub i (s)} newline z sub i = i^th zero newline hat z sub i = conjugate of z sub i newline p sub i = i^th pole

Expanding the numerator and simplifying the result.
n sub i (s) = (s - z sub i)(s - hat z sub i) newline {}=s^2 - (z sub i + hat z sub i)s + z sub i hat z sub i newline {}=s^2 - 2 Re z sub i s + (Re z sub i)^2 + (Im z sub i)^2 newline Re z sub i = real component of z sub i newline Im z sub i = imaginary component of z sub i

In the case of purely imaginary zeros and regular poles the transfer function of the stage can be further simplified.
f sub i(s) = {(s - z sub i)(s - hat z sub i)} over {(s - p sub i)(s- hat p sub i)} = {s^2 + (Im z sub i)^2} over {s^2 - 2 Re p sub i s + p sub i hat p sub i} = {s^2 + "cn0" sub i} over {s^2 + "cd1" sub i s + "cd0" sub i} newline "cn0" sub i = (Im z sub i)^2 newline "cd1" sub i = -2 Re p sub i newline "cd0" sub i = p sub i hat p sub i

Once the stage prototype function is found the bilinear transform can be applied to obtain the digital filter stage at a given frequency.
s drarrow 1 over {tan(%omega/2)} (z-1) over (z+1) = K (z-1) over (z+1) newline %omega = 2 %pi f sub c over f sub s newline f sub c = cutoff frequency newline f sub s = sampling frequency

F sub i(z) = f sub i(K (z-1)over(z+1)) = { ("cn0" sub i+K^2) z^2 + (2 "cn0" sub i - 2 K^2) z + "cn0" sub i + K^2} over { ("cd0" sub i + K "cd1" sub i +K^2) z^2 + (2 "cd0" sub i - 2 K^2) z + "cd0" sub i - K "cd1" sub i + K^2}

This can be converted to a form that is conducive to implementation by a digital filter.
{ ("cn0" sub i+K^2) z^2 + (2 "cn0" sub i - 2 K^2) z + "cn0" sub i + K^2} over { ("cd0" sub i + K "cd1" sub i +K^2) z^2 + (2 "cd0" sub i - 2 K^2) z + "cd0" sub i - K "cd1" sub i + K^2} cdot {z^-2 over z^-2} newline {}= { ("cn0" sub i+K^2) + (2 "cn0" sub i - 2 K^2) z^-1 + ("cn0" sub i + K^2) z^-2} over { ("cd0" sub i + K "cd1" sub i +K^2) + (2 "cd0" sub i - 2 K^2) z^-1 + ("cd0" sub i - K "cd1" sub i + K^2) z^-2} newline {}= { "b0" sub i + "b1" sub i z^-1 + "b2" sub i z^-2 } over { "a0" sub i + "a1" sub i z^-1 + "a2" sub i z^-2 }